## Slide 1
DESIGN & OPTIMIZATION OF EFFICIENT LEAD-FREE PEROVSKITE BASED TANDEM SOLAR CELL
Presented by
Mashrife Jaman Radib
ID : 1802007
Abrar Adib
ID : 1802019
Supervised by Mrinmoy Dey Associate Professor Dept. of EEE, CUET
Department of Electrical and Electronic Engineering Chittagong University of Engineering and Technology

## Slide 2: Presentation Outline
Objectives.
Background and Present State of Problem.
Why Solar Energy.
Methodology.
Design and Simulation of Proposed Tandem Cell.
Results and Discussions.

## Slide 3: Objectives
i. Detailed discussion about the Perovskite tandem solar cell for higher power conversion efficiency
ii. Modeling & simulation of tandem solar cells with Perovskite as top cell and Si, GeTe and CuInSe2 as bottom cell
iii. Performance analysis and comparative study of the proposed tandem solar cells

## Slide 4: Background and Present State of the Problem
Global energy consumption is rising.
The supply of fossil fuels will be over soon.
Global warming.
GHG emission.
Figure 1 : Rising Global Energy Consumption [1]

## Slide 5: Alternative : Renewable Energy Sources
Solar Energy
Wind Energy
Hydro Energy
Biomass Energy
Geothermal Energy
Figure 2 : Renewable Energy Sources

## Slide 6: Solar Energy
Lowers carbon footprint
Figure 3 : Solar Panels
Advances clean energy technology
Supports local economy
Backs up grid energy
Long lifespan

## Slide 7
Evolution of Solar Cells
Figure 5 : Classification of Solar Cells [3]

## Slide 8
Why Perovskite Solar Cell
Lower production cost
Better efficiency
High absorption coefficient
Long diffusion length
Good carrier mobility

## Slide 9
Literature Review of Single Junction Cells
Device Structure | Voc (volts) | Jsc (mA/cm2) | FF (%) | PCE (%) | Ref.
Glass-base / FTO / Cd0.5Zn0.5S / MASnI3 / MASnBr3 / Au | 0.96 | 32.48 | 76.40 | 23.86 | [4]
ITO/ZnO/MASnI3/ CuSbS2/Ag | 0.876 | 33.19 | 76.19 | 22.16 | [5]
FTO/TiO2/MASnBr3/ NiO/Au | 0.80 | 31.88 | 84.89 | 21.66 | [6]
ITO/ZnO/MASnBr3/Spiro-OMeTAD/Au | 1.01 | 32.42 | 75.67 | 25.02 | [7]
FTO/SnO2/MAPbI3/Spiro-OMeTAD/Au | 1.32 | 22.93 | 79.39 | 23.22 | [8]

## Slide 10
Device Structure | Voc (volts) | Jsc (mA/cm2) | FF (%) | PCE (%) | Ref.
CH3NH3PbI3 / CIGS | 1.81 | 20.49 | 81.90 | 30.50 | [9]
CH3NH3PbI3 / GeTe | 1.747 | 25.88 | 79.40 | 35.90 | [10]
CH3NH3PbI3 / Si | 2.11 | 20.95 | 79.45 | 35.30 | [11]
MAGeI3 / FASnI3 | 2.62 | 14.69 | 79.80 | 30.86 | [12]
Literature Review of Tandem Cells

## Slide 11
STEP 01
Selection of Reference Cell
STEP 02
Design and Optimization of Top Cell
STEP 03
Comparison With the Reference Cell
STEP 04
Design and Optimization of Bottom Cell
STEP 06
Perform the Simulation of Tandem Cell
Current Matching Between Two Cells
STEP 05
Methodology

## Slide 12
Reference Cell for Perovskite Top Cell
Figure 7 : Structure and Band Simulation of the Reference Cell [6]
Cells | Voc (V) | Jsc (mA/cm2) | FF (%) | PCE (%)
Reference Cell | 0.80 | 31.88 | 84.89 | 21.66
Our Simulation | 0.78 | 30.43 | 84.35 | 20.03

## Slide 13: Selection of ETL for Perovskite Top Cell
Device Structure | Jsc (mA/cm2) | Voc (volts) | FF (%) | PCE (%)
ITO/TiO2/MASnBr3/Au | 29.53 | 1.06 | 80.37 | 25.22
ITO/WS2/MASnBr3/Au | 29.64 | 1.05 | 79.9 | 25.13
ITO/IGZO/MASnBr3/Au | 29.43 | 1.06 | 80.21 | 25.03
ITO/AZO/MASnBr3/Au | 29.40 | 1.061 | 79.7 | 24.85
Figure 8 : PCE for Various ETL Layers

## Slide 14: Selection of HTL for Perovskite Top Cell
Device Structure | Jsc (mA/cm2) | Voc (volts) | FF (%) | PCE (%)
ITO/TiO2/MASnBr3/CuSbS2/Au | 30.51 | 1.046 | 80.85 | 25.53
ITO/TiO2/MASnBr3/Spiro-OMeTAD/Au | 30.32 | 1.045 | 78.35 | 25.36
ITO/ TiO2/MASnBr3/MoS2/Au | 32.10 | 1.043 | 77.12 | 25.80
ITO/ TiO2/MASnBr3/Cu2O/Au | 30.85 | 1.048 | 80.43 | 26.23
Figure 9 : PCE for Various HTL Layers

## Slide 15: Optimization of MASnBr3 Absorber Layer
Figure 10 : MASnBr3 Absorber layer Thickness
Optimization
Figure 11 : MASnBr3 Absorber layer Doping density
Optimization
Figure 12 : MASnBr3 Absorber layer Doping density
Optimization
Thickness = 500 nm
Acceptor Density = 1×1016/cm3
Defect Density = 1×1013/cm3

## Slide 16: Proposed Structure for MASnBr3 Perovskite Top Cell
Figure 13 : Structure of Perovskite Top Cell
AM 1.5G Spectrum
Thickness = 50 nm
Donor Density = 1×1018/cm3
Thickness = 100 nm
Acceptor Density = 1×1019/cm3
Au
Glass substrate
ITO
TiO2
CH3NH3SnBr3
Cu2O

## Slide 17: Energy Band Alignment Diagram of Perovskite Top Cell
Figure 14 : Energy band alignment diagram of Perovskite Top Cell
MASnBr3
Cu2O
(HTL)
TiO2
(ETL)
Cathode
Anode
e
e
e
E
n
e
r
g
y
L
e
v
e
l
h
h
h
-4.2
-7.46
-4.17
-5.5
-3.2
-5.37

## Slide 18: Simulation Output of MASnBr3 Perovskite Top Cell
Voc (V) | Jsc (mA/cm2) | FF (%) | PCE (%)
1.04 | 30.75 | 80.66 | 26.20
Simulation Output of Optimized Perovskite based Top Cell
Figure 15 : JV curve of MASnBr3 based Top Cell

## Slide 19: Thermal Stability of MASnBr3 Perovskite Top Cell
The temperature coefficient of the perovskite based top cell is found to be about -0.183% per oC.
Figure 16 : Effect of Temperature Variation on Top Cell

## Slide 20
Quantum Efficiency of Perovskite Top Cell
Figure 17 : QE vs wavelength curve of Top Cell

## Slide 21
Comparison of the Optimized Top Cell With Reference Cell
Reference Cell
Proposed Cell
Voc (V) | Jsc (mA/cm2) | FF (%) | PCE (%)
0.80 | 31.88 | 84.89 | 21.66
Simulation Output of Reference Cell
Voc (V) | Jsc (mA/cm2) | FF (%) | PCE (%)
1.04 | 30.75 | 80.66 | 26.20
Simulation Output of Proposed Top Cell

## Slide 22: AM 1.5G and Filtered Spectrum
Figure 18 : AM 1.5G and Filtered Spectrum
The filtered spectrum can be calculated from the following formula :

## Slide 23: Structure of Si Bottom Cell
c-Si (n)
c-Si (p)
c-Si (p+)
Au
Figure 19 : Structure of c-Si Bottom Cell
Filtered/Transmitted Spectrum
Thickness = 50 nm
Donor Density = 1×1019/cm3
Thickness = 100 nm
Acceptor Density = 9.5×1018/cm3
FTO

## Slide 24: Optimization of Si Absorber Layer
Figure 20 : c-Si (p) Absorber layer Thickness
Optimization
Figure 21 : c-Si (p) Absorber layer Acceptor Density
Optimization
Figure 22 : c-Si (p) Absorber layer Defect Density
Optimization
Thickness = 100 μm
Acceptor Density= 1×1015/cm3
Defect Density = 1×1013/cm3

## Slide 25
Simulation Output of Si Bottom Cell
Voc (V) | Jsc (mA/cm2) | FF (%) | PCE (%)
0.56 | 30.85 | 80.65 | 25.84
Simulation Output of Optimized Si Bottom Cell
Figure 23 : JV curve of Si Bottom Cell

## Slide 26: MASnBr3/Si Tandem Cell
Figure 25 : Structure of MASnBr3/c-Si Tandem Cell
Glass Substrate
ITO
TiO2
CH3NH3SnBr3
Cu2O
c-Si (p)
c-Si (p+)
Au
c-Si (n)
FTO
AM 1.5G Spectrum
Filtered/Transmitted Spectrum
The top cell will absorb high energy photons due to its higher energy bandgap.
The lower energy photons are passed on towards the bottom cell and get absorbed.
Top Sub-cell
Bottom Sub-cell

## Slide 27: MASnBr3/Si Tandem Cell
Figure 26 : JV curve of MASnBr3/c-Si Tandem Cell
Structure | Voc (V) | Jsc (mA/cm2) | FF (%) | PCE (%)
Top Cell | 1.04 | 30.75 | 80.66 | 26.20
Bottom Cell | 0.56 | 30.53 | 80.65 | 25.84
Tandem | 1.59 | 30.56 | 80.43 | 38.86
Simulation Output of MASnBr3/Si Tandem Cell

## Slide 28: Structure of GeTe Bottom Cell
FTO
CdZnS
GeTe
Ni
Figure 27 : Structure of GeTe Bottom Cell
Filtered/Transmitted Spectrum
Thickness = 50 nm
Acceptor Density = 1×1018/cm3

## Slide 29: Optimization of GeTe Absorber Layer
Figure 28 : GeTe Absorber layer Thickness
Optimization
Figure 29 : GeTe Absorber layer Acceptor Density
Optimization
Figure 30 : GeTe Absorber layer Defect Density
Optimization
Thickness = 750 nm
Acceptor Density = 1×1015/cm3
Defect Density = 1×1013/cm3

## Slide 30
Voc (V) | Jsc (mA/cm2) | FF (%) | PCE (%)
0.55 | 30.61 | 80.57 | 26.70
Simulation Output of Optimized GeTe Bottom Cell
Figure 32 : JV curve of GeTe Bottom Cell
Figure 31 : Current Matching for GeTe Bottom Cell
Simulation Output of GeTe Bottom Cell
750 nm

## Slide 31: MASnBr3/GeTe Tandem Cell
Figure 34 : Structure of MASnBr3/GeTe Tandem Cell
Glass Substrate
ITO
TiO2
CH3NH3SnBr3
CuSbS2
FTO
CdZnS
GeTe
Ni
AM 1.5G Spectrum
Filtered/Transmitted Spectrum
Top Sub-cell
Bottom Sub-cell

## Slide 32: MASnBr3/GeTe Tandem Cell
Figure 35 : JV curve of MASnBr3/GeTe Tandem Cell
Simulation Output of MASnBr3/GeTe Tandem Cell
Structure | Voc (V) | Jsc (mA/cm2) | FF (%) | PCE (%)
Top Cell | 1.04 | 30.75 | 80.66 | 26.20
Bottom Cell | 0.55 | 30.61 | 80.57 | 26.70
Tandem | 1.59 | 30.62 | 80.58 | 39.20

## Slide 33: Structure of CuInSe2 Bottom Cell
FTO
WS2
CuInSe2
Ni
MoTe2
Figure 36 : Structure of CuInSe2 Bottom Cell
Filtered/Transmitted Spectrum
Thickness = 50 nm
Donor Density = 1×1018/cm3
Thickness = 100 nm
Acceptor Density = 1×1019/cm3

## Slide 34: Optimization of CuInSe2 Absorber Layer
Figure 38 : CuInSe2 Absorber layer Acceptor Density
Optimization
Figure 39 : CuInSe2 Absorber layer Defect Density
Optimization
Thickness = 700 nm
Acceptor Density = 1×1015/cm3
Defect Density = 1×1013/cm3
Figure 37 : CuInSe2 Absorber layer Thickness
Optimization

## Slide 35
Figure 41 : JV curve of CuInSe2 Bottom Cell
Voc (V) | Jsc (mA/cm2) | FF (%) | PCE (%)
0.68 | 30.57 | 82.34 | 30.13
Simulation Output of Optimized CuInSe2 Bottom Cell
Figure 40 : Current Matching for CuInSe2 Bottom Cell
Simulation Output of CuInSe2 Bottom Cell
700 nm

## Slide 36: MASnBr3/CuInSe2 Tandem Cell
Figure 43 : Structure of MASnBr3/CuInSe2 Tandem Cell
Glass Substrate
ITO
TiO2
CH3NH3SnBr3
CuSbS2
FTO
WS2
CuInSe2
Ni
MoTe2
AM 1.5G Spectrum
Filtered/Transmitted Spectrum
Top Sub-cell
Bottom Sub-cell

## Slide 37: MASnBr3/CuInSe2 Tandem Cell
Simulation Output of MASnBr3/CuInSe2 Tandem Cell
Figure 44 : JV curve of MASnBr3/CuInSe2 Tandem Cell
Structure | Voc (V) | Jsc (mA/cm2) | FF (%) | PCE (%)
Top Cell | 1.04 | 30.75 | 80.66 | 26.20
Bottom Cell | 0.68 | 30.57 | 82.34 | 30.13
Tandem | 1.71 | 30.58 | 80.07 | 41.68

## Slide 38
Thermal Stability of the Optimized Bottom Cells
Bottom Cell | Efficiency at Room Temperature (27oC) | Temperature Coefficient (per oC)
Si | 25.84% | -0.50%
GeTe | 26.70% | -0.307%
CuInSe2 | 30.13% | -0.335%
Table : Thermal Stability of the optimized bottom cells
Figure 46 : Thermal Stability of the Bottom Cells

## Slide 39: Results and Discussions
Device Structure | Voc (volts) | Jsc (mA/cm2) | FF (%) | PCE (%) | Ref.
Glass-base / FTO / Cd0.5Zn0.5S / MASnI3 / MASnBr3 / Au | 0.96 | 32.48 | 76.40 | 23.86 | [4]
ITO/ZnO/MASnI3/ CuSbS2/Ag | 0.876 | 33.19 | 76.19 | 22.16 | [5]
CH3NH3PbI3 / CIGS | 1.81 | 20.49 | 81.90 | 30.50 | [9]
CH3NH3PbI3 / GeTe | 1.747 | 25.88 | 79.40 | 35.90 | [10]
CH3NH3PbI3 / Si | 2.11 | 20.95 | 79.45 | 35.30 | [11]
MAGeI3 / FASnI3 | 2.62 | 14.69 | 79.80 | 30.86 | [12]
CH3NH3SnBr3 /Si | 1.59 | 30.56 | 80.43 | 38.86 | This work
CH3NH3SnBr3 /GeTe | 1.58 | 30.63 | 80.58 | 39.20 | This work
CH3NH3SnBr3 /CuInSe2 (proposed) | 1.71 | 30.59 | 80.07 | 41.68 | This work
Table : Comparative study between previously published works and this work

## Slide 40: References
[1] Guan, Y., Yan, J., Shan, Y., Zhou, Y., Hang, Y., Li, R., ... & Hubacek, K. (2023). Burden of the global energy price crisis on households. Nature Energy, 8(3), 304-316.
[2] Zhang, H. L., Van Gerven, T., Baeyens, J., & Degrève, J. (2014). Photovoltaics: Reviewing the European feed-in-tariffs and changing PV efficiencies and costs. The Scientific World Journal, 2014.
[3] Pham, H. D., Yang, T. C. J., Jain, S. M., Wilson, G. J., & Sonar, P. (2020). Development of dopant‐free organic hole transporting materials for perovskite solar cells. Advanced Energy Materials, 10(13), 1903326.
[4] Y. Gan et al., “Numerical Investigation Energy Conversion Performance of Tin-Based Perovskite Solar Cells Using Cell Capacitance Simulator,” Energies (Basel), vol. 13,no. 22, p. 5907, Nov. 2020, doi: 10.3390/en13225907.
[5] S. Bhattarai et al., “Investigation of Carrier Transport Materials for Performance Assessment of Lead-Free Perovskite Solar Cells,” IEEE Trans Electron Devices, vol. 69, no.6, pp. 3217–3224, Jun. 2022, doi: 10.1109/TED.2022.3165516.
[6] Md. Samiul Islam et al., “Defect Study and Modelling of SnX3-Based Perovskite Solar Cells with SCAPS-1D,” Nanomaterials, vol. 11, no. 5, p. 1218, May 2021, doi: 10.3390/nano11051218.
[7] Bala, N., & Mallik, S. K. (2024). Comparative Study of Lead-free Perovskite Materials MASnI3, MASnBr3 and MAGeI3 to Design, Simulate and Optimize Lead Free PSC. Indian Journal of Pure & Applied Physics (IJPAP), 62(4), 292-303.

## Slide 41
[8] Shrivastav, N., Kashyap, S., Madan, J., Al-Mousoi, A. K., Mohammed, M. K., Hossain, M. K., ... & Ramanujam, J. (2023). Perovskite-CIGS monolithic tandem solar cells with 29.7% efficiency: a numerical study. Energy & Fuels, 37(4), 3083-3090.
[9] Salah MM, Zekry A, Abouelatta M, Shaker A, Mousa M, Amer FZ, Mubarak RI, Saeed A. High-Efficiency Electron Transport Layer-Free Perovskite/GeTe Tandem Solar Cell: Numerical Simulation. Crystals. 2022; 12(7):878.
[10] Abedini-Ahangarkola, H., Soleimani-Amiri, S., & Rudi, S. G. (2022). Modeling and numerical simulation of high efficiency perovskite solar cell with three active layers. Solar Energy, 236, 724-732.
[10] Pandey, R., Bhattarai, S., Sharma, K., Madan, J., Al-Mousoi, A. K., Mohammed, M. K., & Hossain, M. K. (2023). Halide composition engineered a non-toxic perovskite–silicon tandem solar cell with 30.7% conversion efficiency. ACS Applied Electronic Materials, 5(10), 5303-5315.
[11] Mondol, N., Islam, K. S., Islam, M. R., & Das, S. K. (2024). Enhancing solar cell efficiency: Investigation of high-performance lead-based perovskite-on-silicon (PVK–Si) tandem solar cells through design and numerical analysis. AIP Advances, 14(1).
[12] El Arfaoui, Y., Khenfouch, M., & Habiballah, N. (2024). HTL-free non-toxic perovskite tandem solar device MAGeI3/FASnI3 with 25.69% efficiency: design and simulation using SCAPS. Journal of Optics, 1-14.
References

## Slide 42
Thank You
Any Questions?